УДК 543:552.054.1:543.3:546

И.Н. Сенчакова, Э.Ю. Юшкова, Э.Р. Оскотская

Определение подвижных форм хрома в техногенных водах

Аннотация. В работе изложены результаты исследований аналитических параметров предварительного концентрирования Cr (III) и Cr (VI), сорбентами на полистирольной матрице, химически модифицированной различными функциональными группами. Экспериментально изучена избирательность их действия и возможность десорбции различных форм хрома с сорбентов. В статье представлены данные о количественном определении хрома в сложных по химическому составу техногенных водах с помощью разработанной комбинированной сорбционно-спектрофотометрической методики.

Ключевые слова: хром, предварительное концентрирование, сорбенты, определение, техногенные воды.

Литература

1. Методика измерений массовой концентрации ионов хрома в питьевых, природных и сточных водах фотометрическим методом с дифенилкарбазидом ПНД Ф 14.1:2:4.52-96, Москва 2016 г.

2. Оскотская, Э.Р. Сорбционное концентрирование хромат-, нитрат- и селенит-ионов и их определение в природных и сточных водах / Оскотская Э.Р., Юшкова Э.Ю., Басаргин Н.Н. // Ученые записки Орловского государственного университета. – 2007. – No2. – С. 47 – 55.

3. Оскотская Э.Р., Басаргин Н.Н., Сенчакова И.Н., Юшкова Э.Ю., Осипова А.В. Концентрирование и определение Сr (III) и Cr (VI) в природных и сточных водах / VII Всероссийская конференция по анализу объектов окружающей среды «ЭКОАНАЛИТИКА 2009», 21-27 июня 2009 г., Йошкар-Ола, – С. 163.

4. ГОСТ 31956-2012 (ИСО 9174:1998, ИСО 11083:1994, ИСО 18412:2005) Вода. Методы определения содержания хрома (VI) и общего хрома. – М.: Стандартинформ, – 2012. – 43 с.

UDC 543:552.054.1:543.3:546

I. N. Senchakova, E. Y. Yushkova, E. R. Oskotskaya

Determination of mobile forms of chromium in technogenic waters

Key words: chromium, pre-concentrate, sorbents, definition, technogenic waters.

Abstract. In the paper the research results of studies of the analytical parameters of preconcentration of Cr (III) and Cr (VI) by sorbents on a polystyrene matrix, chemically modified by various functional groups are presented.  The selectivity of their action and the possibility of desorption of various forms of chromium from sorbents have been experimentally studied. The article presents the data on the quantitative determination of chromium in a complex chemical composition of technogenic waters with the help of the developed complex sorption-spectrophotometric technique.

References

1. The method of measurement of mass concentration of chromium ions in drinking, natural and waste waters by photometric method with diphenylcarbazide PND f 14.1:2:4.52-96, Moscow, 2016.

2. Oskotskaya, E. R. Sorption preconcentration of chromate-, nitrate- and selenite- ions and their determination in natural and waste waters / Oskotskaya E.R., Yushkova E.Y., Basargin N.N. // Scientific notes of Orel state University. – 2007. – no 2. – pp. 47 – 55.

3. Oskotskaya ER, Basargin NN, Senchakova I.N., Yushkova E.Y., Osipova A.V.  Concentration and determination of Cr (III) and Cr (VI) in natural and waste waters / VII All-Russian Conference on the Analysis of Environmental Objects "ECOANALYTICS 2009", June 21-27, 2009, Yoshkar-Ola, -P. 163.

4. GOST 31956-2012 (ISO 9174: 1998, ISO 11083: 1994, ISO 18412: 2005) Water.  Methods for determining the content of chromium (VI) and total chromium.  - Moscow: Standartinform, - 2012. - 43 p.

| Э.Р. Оскотская– д.х.н., профессор, зав.каф. химии, Орловский государственный университет имени И.С. Тургенева е-mail: osckotskaya@yandex.ru | E.R. Osckotskaya - doctor of chemistry sciences, professor, Department of Сhemistry, Turgenev Orel State University е-mail: osckotskaya@yandex.ru |
| --- | --- |
| И.Н. Сенчакова– к.х.н., доцент кафедры химии, Орловский государственный университет имени И.С. Тургенева е-mail: irinka-sen@mail.ru | I.N. Senchakova - candidate of chemistry sciences, associate professor, Department of Сhemistry, Turgrnev Orel State University е-mail: irinka-sen@mail.ru |
| Э.Ю. Юшкова– к.х.н., доцент кафедры химии, Орловский государственный университет имени И.С. Тургенева е-mail: savally2@gmail.com | E.Y. Yushkova - candidate of chemistry sciences, associate professor, Department of Сhemistry, Turgrnev Orel State University е-mail: savally2@gmail.com |